Detailed Clinical Models, Medical Devices Domain

Use Case

Intubate Patient, Unplanned

Revision History

| Date | Version | Description | Author | SMEs |
| --- | --- | --- | --- | --- |
| 7/22 | 0.3 | Modifications based on team call | Jay Lyle |  |
| 7/20/10 | 0.2 | Additional description for case & actors, extensions removed (comments from IS); revisions to data for settings (7/20 meeting) | Jay Lyle |  |
| 7/16/2010 | 0.1 | Initial Draft | Jay Lyle |  |

# Document Purpose

This is an interoperability use case designed to define interactions between clinicians and ventilators and other devices and systems in the interest of developing an information model to support those interactions. This model may contain or reference one or more “detailed clinical models” (DCMs)--a formalism for representing clinical information currently under development. Confirming the method for using these component models is a key goal of the project sponsoring the use case. The requirement for clinical accuracy in DCMs means that the scope of the information model extends beyond the device interactions to other clinical facts: these facts are bounded in this case by the VA National Template for Intubation and by the Advanced Cardiac Life Support protocol published by the American Heart Association.

# Use Case Description

In response to an ICU patient’s deteriorating condition, a team of clinicians intubates a patient and attaches the patient to a ventilator, confirms that the ventilator is working properly, and confirms that the settings are correct.

This use case explicitly excludes planned intubations, typically performed prior to surgery, and the involvement of an anesthesiologist.

# Actors

- Clinician with intubation privileges – a clinician of any title who is permitted to perform intubations

- Response team member: other clinician, with or without intubation privileges, including

  - Nurse – typically responsible for patient care; may assist with intubation process

  - Respiratory Therapist – typically responsible for setting up the ventilator and modifying settings

  - MD – A physician who may have ordered the intubation and may assist with intubation process

- Patient: The patient has no responsibilities in the workflow, and so is not formally considered an actor. However, the patient is an important participant.

# Systems and Devices

- Ventilator

- Arterial Blood Gas monitor

- Pulse Oximeter

- Electrocardiograph

- Vital signs monitor

- Capnometer

- X-ray

- Laryngoscope

- Electronic Health Record (local, partial, or comprehensive)

# Trigger

In response to a deterioration in patient condition, a physician orders intubation (verbally or in a document) and assembles a team.

- Order or protocol for intubation

# Pre-Conditions

- Patient ID: patient admitted to room system

  - Any system independently identifying the patient, e.g., via barcode, will also already have identified the patient.

- Pre-medication

- Assessment

- Equipment

  - Ventilator on

  - Monitors attached

- Supplies for airway management on hand

# Post Conditions

If the use case was completed, then

- Patient condition

  - Endotracheal (ET) tube placement verified and secured

  - Patient assessed for response to intubation

- Ventilatory status

  - Ventilator parameters are set

  - Equipment alarms are set

- EHR documentation

  - All setup readings and settings in EHR

- Ongoing monitoring

  - Patient observations are sent to EHR on the specified schedule

# Workflow

## ICU Emergency Workflow

This workflow is based on the clinical scenario referenced in section 11.

|  | Actor | Action | System Response |
| --- | --- | --- | --- |
| 1. | Privileged clinician | Decide to intubate |  |
| 2. | Privileged clinician | Call team |  |
| 3. | Response team member | Sedate patient |  |
| 4. | Response team member | Assemble supplies |  |
| 5. | Response team member | Prepare patient position |  |
| 6. | Response team member | Assess patient | Vitals monitor: display vitals ABG: display ABGs [note] EKG: display EKG Pulse oximeter: display O2 |
| 7. | Privileged clinician | Intubate patient | Laryngoscope: record intubation |
| 8. | Response team member | Confirm placement by sound |  |
| 9. | Response team member | Confirm placement by CO2 measurement | Capnometer: Display EtCO2 |
| 10. | ? | Confirm placement by x-ray | X-ray: Display image X-ray: Record image |
| 11. | Response team member | Begin manual ventilation (bag valve mask) |  |
| 12. | Response team member | Attach ventilator to electricity, air, and oxygen |  |
| 13. | Response team member | Confirm ventilator self-test | Ventilator: display confirmation |
| 14. | Response team member | Place ventilator on standby | Ventilator: display mode |
| 15. | Response team member | Determine settings and confirm |  |
| 16. | Response team member | Enter settings | Ventilator: display settings |
| 17. | Response team member | Take ventilator off standby | Ventilator: display mode |
| 18. | Response team member | Connect patient to ventilator |  |
| 19. | Response team member | Connect ventilator to medical record | Ventilator: record mode & settings |
| 20. | Response team member | Set alarms | Ventilator: record alarms |
| 21. | Response team member | Assess patient | As above |
| 22. | Response team member | Document intubation | EHR: record intubation procedure |

Notes:

- All steps: information regarding these steps to be recorded manually after intubation is noted below, based on the VA National template.

- Step 1: Decision may be based on blood gas threshold alarm, notification from laboratory, or other clinical factor. Clinical observation values are not part of the ventilator communication at this point: see the Manage Ventilator case for more detail.

  - Template: “Primary conditions requiring tracheal intubation,” 10 values

- Step 2: Calling the team may involve the use of a “code” or “rapid response” call; in the (ideal) subtending scenario, the patient is in the ICU and no assembly is required.

  - Template: title of person performing intubation, degree of supervision, location, emergent status

- Step 3: medication will vary depending on available clinician’s privileges and urgency of process.

  - Template: sedation (5 values plus “none” and “other”), Neuromuscular blocking agent (6 values plus “none” and “other”), and “Other pharmacological agents utilized during intubation”

- Step 4: supplies are on hand in ICU.

- Step 5: preparation involves patient position, bed configuration, and any other object obstructing team members from putting the ventilator and tube into position for use.

- Step 7: intubation may be assisted with a laryngoscope or other device, none of which are currently capable of detecting or recording information.

  - Template: instrumentation, insertion route, tube size, Cormack/Lehane scale, success indicator, attempt count, esophageal intubation count

- Steps 8-10: confirmation may follow different paths, one step of which may result in an interaction.

  - Template: “confirmation by” CO2, EDD, both, or neither; “post-procedure chest x-ray ordered.”

- Step 13: Ventilator self-tests and confirms readiness, but this is not made part of the record.

- Step 16: Settings will be communicated to the patient record. Will this be only on setting changes, with any reading, or some other schedule?

- Step 19: In this scenario, the ventilator automatically sends information to the EHR. In many ICUs this will not be true.

- Step 20: alarm settings—need more detail

# Data

All Case Steps: baseline metadata for all observations and instructions

Device All

| Field Name | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- |
| Device type |  |  |  |
| Device model |  |  |  |
| Interaction time |  |  |  |
| Clinician responsible | Name? BL? |  |  |
| Time of clinician confirmation |  |  |  |
| Patient identifier |  |  |  |

All Case Steps: baseline metadata for all observations

Device All

| Field Name | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- |
| Observation Method |  |  |  |
| Time of observation | Time |  |  |

Case Step 5: Confirm Observations

Device Vitals monitor

| Field Name | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- |
| Heart rate | Integer (1/min) | 80 |  |
| Respiratory rate | Integer (1/min) | 20 |  |
| Temperature | Float, degrees | 37, 98.6 |  |
| Blood pressure | String or model | 120/90 | How complex should this be? Include position, method, cuff size, other process or device information? Or should we import the existing BP DCM? |

Case Step 5: Confirm Observations

Device Pulse Oximeter

| Field Name | Description | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- | --- |
| SpO2 | Arterial saturation of hemoglobin | % | 95 |  |

Case Step 5: Confirm Observations

Device: Arterial blood gas monitor

| Field Name | Description | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- | --- |
| SaO2 | Arterial saturation of hemoglobin and other globins | % | 95 |  |
| PaO2 | Oxygen pressure of plasma | mmHg |  |  |
| pH | Acidity | Float | 7.5 | Do we care about significant digits? |
| PaCO2 | CO2 pressure of plasma | mmHg | 35-45 |  |
| PO2 |  |  |  | Alveolar pressure? “PO2” mentioned on call but not confirmed by cross-reference—possibly a local shorthand or idiom? |

Case Step 5: Confirm Observations

Device EKG

| Field Name | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- |
| EKG snapshot | Image file |  |  |
| Parameters? |  |  |  |

Case Step 6: Intubate Patient

Device Pulse Laryngoscope

| Field Name | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- |
| Intubation video | Video file |  |  |
| Parameters? |  |  |  |

Case Step: 8 Display EtCO2

Device Capnometer

| Field Name | Description | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- | --- |
| EtCO2 | End-tidal CO2, or percentage of CO2 in exhaled air | Percent Or mmHg? | 5% 35-37 mmHg | Single value taken to establish intubation |

Case Step 9: Record EtCO2

Device: Capnometer

| Field Name | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- |
| EtCO2 observation | Percent Or mmHg? | 5% 35-37 mmHg | Single value taken to establish intubation |

Case Step 19: Record Settings

Device: Ventilator

| Field Name | Description | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- | --- |
| Mode |  | Enumerated | Assist Control (AC) | Mode affects required settings |
| RR | Respiratory rate | Integer (1/min) | 12-16 | May be set as target EtCO2 level in a closed loop system |
| Vt | Tidal volume | Integer (mL) | 10-12 mL/kg; .3 to .7 L | Varies by protocol and patient |
| FiO2 | fraction of inspired O2 | Percent | 60% | Varies by protocol and patient |
| PEEP | Positive expiratory end pressure | cmH2O | 5 | Varies by protocol and patient |
| PS | Pressure Support |  |  | Not included in AC mode |
| Inspiratory flow rate |  | Integer (L/min) | 40-60 | Peak value; varies by protocol and patient |
| I:E | In-to-out ratio |  |  | Not set for AC: use flow rate and inspiratory time instead |
| Inspiratory time |  |  |  | Not specified but implied by I:E comment |
| Waveform |  | Enumerated | Decelerated |  |
| Sensitivity pressure target |  | cmH2O | 2-5 |  |
| Flow trigger |  | Float? (L/min) | 1-3 | Won’t be used while paralyzed |
| Setting effective time |  |  |  |  |
| Setting provider name |  |  |  |  |

Case Step 20: Enter Alarm Settings

Device: Ventilator

| Field Name | Data type | Typical Value | Constraints & Notes |
| --- | --- | --- | --- |
| High pressure limit | cmH2O | 15 above PIP | We didn’t set PIP |
| Low pressure limit | cmH2O | 5 above PEEP |  |
| High minute volume | Integer (L/min) | Set + 50% |  |
| Low minute volume | Integer (L/min) | Set/2 |  |
| High RR | Integer (1/min) | Normal + 15 |  |
| Destination? |  |  |  |

Case Step 22: Document intubation (per VA National Template)

Device: EHR

| Field Name | Description | Data type | Constraints & Notes |
| --- | --- | --- | --- |
| Progress note title | “Endotracheal intubation note” |  | Three orthographical variants: significant? |
| Patient | Name, identifier |  | Display only |
| Date | 3 enumerations for M, D, Y | Date | Date only, not time |
| Allergies |  |  | Display only |
| Staff name |  | Text entry |  |
| Job title |  | Enumerated (1) |  |
| Degree of airway supervisory staff involvement |  | Enumerated (1) |  |
| Urgency of procedure |  | Enumerated (1) |  |
| Intubation location |  | Enumerated (1) | Ward in hospital, not approach site |
| Primary conditions requiring tracheal intubation |  | Enumerated (N) |  |
| Reintubation within 24 hours of extubation |  | Yes/No |  |
| Sedation |  | Enumerated (N) | Drug used, or “none” or “other” |
| Neuromuscular blocking agent |  | Enumerated (N) | Drug used, or “none” or “other” |
| Other pharmacological agent used |  | Yes/No | May also include text field for entry if “yes” |
| Instrumentation |  | Enumerated (1) | Tools to assist placement |
| Procedure notes: insertion |  | Enumerated (1) | Approach site |
| Procedure notes: tube size |  | Enumerated (1) |  |
| Procedure notes: View by Cormack / Lehane scale |  | Enumerated (1) |  |
| Procedure notes: Was tracheal intubation successful? |  | Yes/No |  |
| Procedure notes: Number of laryngoscopy attempts |  | Enumerated (1) | 0-3, >3 |
| Procedure notes: Esophageal intubatinos |  | Enumerated (1) | 0-2 |
| Procedure notes: Confirmation method |  | Enumerated (1) | Post-coordinated: CO2, EDD, both, or neither |
| Procedure notes: Condition after procedure |  | Enumerated (1) |  |
| Procedure notes: Other procedural technical notes |  | Yes/No | May also include text field for entry if “yes” |
| Post-intubation patient disposition |  | Enumerated (1) |  |
| Complications |  | Yes/No |  |
| Post-procedure X-ray ordered |  | Yes/No |  |
| Overall difficulty of placement |  | Enumerated (1) |  |
| Plan/ Recommendations |  | Yes/No |  |
| Plan/ Recommendations |  | Text entry |  |

Case Step 22: Document intubation (per ACLS protocol)

Device: EHR

| Field Name | Description | Data type | Constraints & Notes |
| --- | --- | --- | --- |
| EKG |  |  |  |
| B/P |  |  |  |
| Pulse Oximetry |  |  |  |
| EtCO2 |  |  |  |

This section will require further review

# Issues

| Issue Description | Responsible Party | Status |
| --- | --- | --- |
| Variability of device configurations prevents coherent description of scenario Proposed resolution: adopt one real configuration for the scenario to ensure stability in the description, understanding that other scenarios may complicate the case in the future. Choose the best real configuration in order to model a realistic yet desirable state. Alternate: model in as granular a form as possible. Integrated devices can simply play more than one role. | CHoang | Closed 7/22: alternate adopted |
| For data elements without steps, what is their connection to the use case? (E.g., vital signs: obviously important, but do they affect the ventilator device interoperability case?) Resolution: scope beyond devices is determined by documents 5 & 6, below. |  | Closed 7/22 |
| Document 6 provides minimal guidance on information capture: confirm protocol requirements with SME community |  | Open |
| How closely do we relate data from interactions to the larger context? E.g., if a clinician checks “CO2” as a method of confirmation in the CPRS Template, is there an automatic relationship to the capnometer reading? A manually defined one? |  | Open |
| Need to confirm method of confirmation: at device or at EHR. Resolution: at EHR |  | Closed 7/22 |
| Confirm assumption that all devices in the room are associated with the patient admitted to the room; no patient identification is necessary. Resolution: true, as long as we add a ‘barcode’ concept as a precondition. Individual devices requiring barcode patient identification will be assumed to be in the ‘identified’ state. |  | Closed 7/22 |
| Use case identifies clinical data requirements, and also identifies procedural data requirements to the extent that the flow implies them. To what extent is this information already modeled in existing specifications? We assume that device-specific elements (model, calibration date) are out of scope; what of method, sample size (e.g., for ekg), and other elements with both device-specific and clinical meaning? |  | Open |
| Is there an ABG monitor in this scenario, or are we getting ABG readings from a lab? |  | Open |
| We need to confirm PIP setting in workflow to support high pressure limit alarm. Currently it’s not specified. |  | Open |
| Confirm O2 saturation observations: SaO2 was specified: I believe this is a broader measure than SpO2 and is taken by a lab co-oximeter, not a pulse oximeter. “PO2” was also mentioned, which is alveolar partial pressure, which I don’t think is right. Could this be a local idiom for another value? Or was someone saying “PaO2” and I misunderstood? |  | Open |
| Is X-ray taken by any team member, or by a radiology technician? |  | Open |
| Should blood pressure include information apart from systolic and diastolic measures, such as position, method, etc.? Or do we infer that from the device type and clinical circumstances? |  | Open |
| Will the ventilator confirm the connection to the record? To those present, or to the record? |  | Open |
| Are mode changes written to the patient record? |  | Open |
| Are ventilator settings recorded with the name or identifier for the RT or other clinician who set them? |  | Open |
| Is EtCO2 reported as % or mmHg? |  | Open |

# Sources

- Clinical Scenario drafted by Donna DuLong and Catherine Hoang

- Meeting with subject matter experts, 13 July 2010

- Meeting with subject matter experts, 16 July 2010

- Meeting with subject matter experts, 20 July 2010

- Endotracheal Intubation Template from National, provided by Warren Rose RRT, Critical Program Leader, Tampa, Florida

- ACLS protocol document found here